## Slide 1: General Optimization Techniques and Noteworthy Applications for the Altera FPGA OpenCL SDK
Derek Z H Yan
(derek.zh.yan@stanford.edu)
MSEE Candidate Stanford University
Advanced Design Engineer, Altera Corp

## Slide 2: Motivation
FPGA programming paradigm limited to RTL?
  De-facto standard: Verilog HDL/VHDL
  Xilinx Vivado Design Suite: v2012.2 first released May 2, 2012
  Altera OpenCL SDK: v13.0 first released on May 6, 2013
  Xilinx OpenCL?: announced development mid-September, 2013
High performance domain-specific-language realizations on new classes of hardware
  Stanford Delite framework
This work -> Targeting DSL through Delite to FPGA
    OpenCL code generation
    Implementation patterns and optimizations
    High-performance applications

## Slide 3: Outline
Motivation
Overview of Altera OpenCL SDK Design Flow
Optimization and Implementation Strategy Guidelines for Altera OpenCL SDK
High-Performance Applications Suited for Altera OpenCL SDK
Conclusions & Recommendations

## Slide 4: Conventional FGPA Design Flow
VHDL/Verilog HDL Design Entry
Functional Simulation
Synthesis
Place and Route
Static Timing Analysis
On-board verification
always @ (*) begin
case (sel)
2’b00: mux_out = a;
…
LE
DSP
M20K
I/O
tclk

## Slide 5: Heterogeneous Systems for Altera OpenCL SDK
OpenCL
Host Program + Kernels
Bitstream
x86,Power
AOC + Quartus II
Standard C Compiler

## Slide 6: Simplified OpenCL System Architecture
FPGA
Kernel Pipeline
Kernel Pipeline
Kernel Pipeline
PCIe
DDR*
x86 /
External Processor
External
Memory Controller
& PHY
M9K
M9K
M9K
M9K
M9K
M9K
Global Memory Interconnect
Local Memory Interconnect
External
Memory Controller
& PHY
External Interface

## Slide 7: Simplified External Interface
PCIe
DMA
DDR Controller
K0
K1
K2
Kn
Kernel Pipelines

## Slide 8: Simplified Interconnect Architecture
Kernel 1
Kernel 2
load
load
store
store
load
store
Memory
arb2
arb2
arb2
arb2
arb2
Simple arbitration node
Customized pipelining: higher fmax → more throughput

## Slide 9: Altera OpenCL Compiler Flow
kernel.cl
host.c
CLANG
front end
System Description
C compiler
Altera
Runtime
Library
program.exe
Optimizer
Unoptimized LLVM IR
Optimized LLVM IR
RTL generator
Verilog
PCIe
DDR*
OpenCL
Platform
CLANG
front end
Unoptimized LLVM IR
Front End
Parses OpenCL extensions and intrinsics – produces LLVM IR

## Slide 10: Altera OpenCL Compiler Flow Ctd.
kernel.cl
host.c
CLANG
front end
C compiler
Altera
Runtime
Library
program.exe
Optimizer
Unoptimized LLVM IR
Optimized LLVM IR
PCIe
DDR*
OpenCL
Platform
Optimizer
Optimized LLVM IR
Middle End
~150 compiler passes such as loop fusion, auto vectorization, and branch elimination leading to more efficient HW
RTL generator
Verilog

## Slide 11: Altera OpenCL Compiler Flow Ctd.
kernel.cl
host.c
CLANG
front end
C compiler
Altera
Runtime
Library
program.exe
Optimizer
Unoptimized LLVM IR
Optimized LLVM IR
RTL generator
Verilog
PCIe
DDR*
QSYS
Quartus
RTL generator
Verilog
Back End
Instantiate Verilog IP for each operation in the intermediate representation
Create control flow circuitry to handle loops, memory stalls and branching
Traditional optimizations such as scheduling and resource sharing

## Slide 12: Target Heterogeneous Systems Via Delite and OpenCL

## Slide 13: Possible Methods of Attack
OpenCL Code Generator
  Implementation patterns for Altera OpenCL SDK
  Necessary optimizations and
  High-performance applications and comparisons across other heterogeneous platforms
LLVM-IR
  Altera OpenCL converted to HDL through LLVM IR
  Other hardware platforms also consume LLVM IR
Scripting Languages to HDL Converters
  Python-HDL one stop solution

## Slide 14: Altera OpenCL SDK Implementation Patterns and Optimizations
*Slides mainly based on Altera OpenCL Optimization guide and internal Altera training documentations, which can be found at here

## Slide 15: Possible Optimizations:
Intro
Exploiting data-level parallelism
Exploiting task-level parallelism
Exploiting single-work item parallelism
Optimizing Memory Usage
Optimizing Channel Communications

## Slide 16: Deeply Pipelined Kernel Design
GPU Architecture for OpenCL
  Warps of threads of with replicated hardware
  Each thread performs small and identical calculation
  Hybrid of thread and memory level parallelism
FPGA Architecture for OpenCL
  Limited area and complex routing
  Instead, aim for deeply pipelined kernel design to reuse hardware and achieve parallelism
  Pipeline level parallelism

## Slide 17: Deeply Pipelined Kernel Design Ctd.
__kernel void vectorAdd( __global const float *x,
__global const float *y,
__global float *z)
{
int index = get_global_id(0);
z[index] = x[index] + y[index];
}
Vector Add Example:
GPU Implementation:
FPGA Implementation:
Load
Load
Store
0
1
+
Thread n-1
…
Load
Load
Store
+
Thread 0
Load
Load
Store
+
Thread n-1
…

## Slide 18: Good Programming Practices
Avoid branches (generally*)
Avoid work-item dependent backward branching
  Ex. for (size_t i = 0; i < get_global_id(0); i++) {}
Avoid pointer aliasing (use restrict flag)
  May cause non-deterministic behaviors
Use small and inexpensive functions
  Inexpensive functions: binary logic operations (with a constant), shift by a constant (mult/div by a power of 2)
  Expensive functions: integer divide, modulo, floating point divide, atomic functions
Reuse results whenever possible

## Slide 19: Good Programming Practices Ctd.
Floating point optimizations
  Manually enabled and not compliant to IEEE Standard (IEEE 754-2008)
  Flag: aoc –fp-relaxed=true <kernel>.cl
    Apply tree balancing to reduce computation cycles
  Flag: aoc –fpc <kernel>.cl
    Apply rounding only at the end of tree operation
    Reduce hardware
Fixed point optimizations
  Always use less logic than floating point
  Data resolutions limited to (char-8bit, short-16bit, int-32bit, and long-64bit)
  If data resolution doesn’t comply to these bits, use appropriate masking operations to save on hardware

## Slide 20: Good Programming Practices Ctd.

## Slide 21: Exploiting Data Level Parallelism

## Slide 22: Loop Unrolling

## Slide 23: Static Memory Coalescing

## Slide 24: Kernel Vectorization

## Slide 25: Compute Unit Replication

## Slide 26: Exploiting Task Level Parallelism

## Slide 27: Simultaneous Multi-Threading by Multiple Queues

## Slide 28: Synchronization Techniques

## Slide 29: Profiling Tasks Using Events

## Slide 30: Exploiting Single Work Item Parallelism

## Slide 31: Loop Pipelining

## Slide 32: Task Programming Guidelines

## Slide 33: Altera OpenCL SDK Applications and their Relative Performance
*Slides based on investigations of existing OpenCL design examples, which can be found at here

## Slide 34: Sobel 2D Image Filter
Exploits single-work item parallelism
Loop pipelining
Coalesced memory access